## Slide 1
APEX
Machine Learning–Based Prediction of
Aerodynamic Heating on
Satellite Solar Panels
B.Tech Course Project | 2025–26
TEAM APEX
CFD / ANSYS: Ramaraju & Sri Varsha
ML & Validation: Manogna & Praneetha
Documentation: All Members

## Slide 2
INTRODUCTION
Why Thermal Prediction for Satellite Solar Panels?
2 / 17
LEO Environment
Satellites orbit at ~400–2,000 km
Speed: ~7.5 km/s
Solar irradiance: 1,000–1,400 W/m²
No atmospheric filtering
No Convection in Space
Vacuum environment → zero convective
heat transfer. Only conduction &
radiation can remove heat from panel.
High Thermal Load
Panel absorbs 80–85% of solar energy
as heat. Silicon cells lose ~0.45%/K
efficiency above 298 K.
HEAT TRANSFER IN ORBIT
Solar Flux
1,000 W/m² input
Conduction
Through panel layers
Radiation
Only heat escape path
Convection
ABSENT — vacuum
→ Accurate thermal prediction is critical for reliability

## Slide 3
3 / 17
Problem Statement
What are we solving?
Given solar irradiation (W/m²) and ambient temperature (K), predict the maximum temperature of a satellite solar panel — without running a full CFD simulation.
CFD is accurate
but slow
One simulation = hours
Needs 100s of runs for ML data
No convection
in space
Radiation is the only
heat escape path
Temperature
affects efficiency
Efficiency drops ~0.45%/K
above 298 K
SOLUTION → Train ML models as fast, accurate surrogates for CFD thermal simulation

## Slide 4
OBJECTIVES
Project Objectives
4 / 17
01
Perform steady-state thermal simulation of multi-layer PV module in ANSYS under LEO conditions
02
Generate temperature distribution and heat flux data to understand panel thermal behaviour
03
Train 6 ML regression models on a 1,757-sample solar dataset to predict panel max temperature
04
Evaluate models using CV R², Test R², MAE, and RMSE; identify best-performing model
05
Deploy an interactive web dashboard for real-time 3D prediction and model comparison

## Slide 5
ANSYS SIMULATION
Thermal Analysis — ANSYS Setup
5 / 17
Tempered Glass (3.2 mm)
k = 1.0 W/m·K | ε = 0.90
EVA Encapsulant (0.5 mm)
k = 0.35 W/m·K | Transparent
Silicon Cells (0.2 mm)
k = 148 W/m·K | α = 0.90 ← Heat source
EVA Encapsulant (0.5 mm)
k = 0.35 W/m·K
Polymer Backsheet (0.3 mm)
k = 0.2 W/m·K | ε = 0.85
Aluminium Frame (~30 mm)
k = 160 W/m·K | Structural + heat spreader
☀ Solar flux: 1,000 W/m² (top surface)
BOUNDARY CONDITIONS
▸ Solar heat flux: 1,000 W/m² (top glass)
▸ Radiation to deep space: sink = 3 K
▸ No convection (vacuum)
▸ Analysis type: Steady-State Thermal

## Slide 6
SIM RESULTS
ANSYS Simulation Results
6 / 17
[ Temperature Contour — ANSYS ]
Max temp at silicon cell centres
Min temp at frame edges
Max Temp
313–338 K
Hotspot
Silicon layer
Heat path
Glass → EVA → Si → Backsheet → Frame
Limitation
Single simulation = 1 data point.
Needs 100s of runs for ML training.
[ Figure: ANSYS Mesh — 1,640×992 mm panel, automatic sizing on silicon cells ]

## Slide 7
7 / 17
Transition to Machine Learning
Why move from CFD to ML?
CFD SIMULATION ALONE
✕ Single simulation → only 1 data point
✕ Parametric sweep → 100s of runs needed
✕ Each run = hours of compute time
✕ Solver setup issues limited available data
REAL-WORLD DATASET + ML
✔ 1,757-sample real-world solar dataset
✔ Physics-consistent correlations validated
✔ Covers full operating range (0–1,200 W/m²)
✔ ML trains in seconds once data is ready
→
CFD validates physics | Real-world dataset enables robust ML training | Both are complementary

## Slide 8
DATASET
Dataset Description
8 / 17
1,757
Total Samples
2
Input Features
1
Target Variable
80 / 20
Train / Test Split
PRIMARY FEATURE
irradiation_wm2
W/m²
Solar power per unit area
incident on panel surface
r = 0.979 with T_max
SECONDARY FEATURE
ambient_temp_k
Kelvin (K)
Environmental temperature
surrounding the panel
r = 0.631 with T_max
TARGET VARIABLE
max_temp_k
Kelvin (K)
Maximum temperature attained
by the PV panel (TARGET)
Range: ~285–380 K
Source: APEX_Master_Dataset_noisy_v2.csv | Physics-informed synthetic dataset with real-world solar operating conditions

## Slide 9
PREPROCESSING
Data Preprocessing
9 / 17
01
Data Loading & Cleaning
1,757 rows loaded
from CSV
Columns auto-standardised
(lowercase, strip)
No missing values
detected
→
02
Feature Selection
Features (X):
irradiation_wm2,
ambient_temp_k
Target (y):
max_temp_k
Correlation: r = 0.979
& r = 0.631
→
03
Train / Test Split
80% Train → 1,405
samples
20% Test → 352
samples
random_state = 42
(reproducible)
→
04
Feature Scaling
StandardScaler:
zero-mean, unit-var
Applied to: KNN,
SVR only
Fit on train only
→ no data leakage
Key principle: Scaler fit on training data only → applied to test set → prevents data leakage

## Slide 10
ML MODELS
Machine Learning Models Used
10 / 17
Parametric
Multiple Linear
Regression
Predicts T_max as weighted
sum of irradiation +
ambient temp. Interpretable.
Kernel-based
SVR
(RBF kernel)
Fits ε-insensitive tube.
RBF kernel handles
nonlinear patterns.
Instance-based
KNN
(k = 5)
Predicts from 5 nearest
neighbours in feature
space. Non-parametric.
Tree-based
Decision
Tree
Recursive feature splits.
Interpretable but prone
to overfitting.
Ensemble-boost
AdaBoost
(100 estimators)
Boosting ensemble.
Focuses on hard samples
sequentially.
Ensemble-bag
Random
Forest (200 trees)
Bagging ensemble.
Averages 200 trees,
low variance.

## Slide 11
EVALUATION
Model Evaluation & Comparison
11 / 17
CV R²
(5-fold)
Generalisation on
training data
Test R²
Variance explained
on unseen data
MAE (K)
Average prediction
error in Kelvin
RMSE (K)
Penalises large
errors more
Model
CV R²
CV Std
Test R²
MAE (K)
RMSE (K)
Multiple Linear Reg.
0.9708
±0.0024
0.9641
3.43
4.30
SVR (RBF kernel)
0.9706
±0.0023
0.9635
3.44
4.34
KNN (k=5)
0.9641
±0.0019
0.9577
3.77
4.67
Random Forest
0.9634
±0.0025
0.9572
3.70
4.70
AdaBoost
0.9623
±0.0016
0.9519
3.97
4.98
Decision Tree
0.9363
±0.0030
0.9347
4.45
5.80
★ Best Model: Multiple Linear Regression | Test R² = 0.9641 | MAE = 3.43 K | RMSE = 4.30 K

## Slide 12
RESULTS
Results — Best Model Performance
12 / 17
0.9641
Test R²
96.41% variance explained
3.43 K
Mean Abs. Error
Average prediction error
4.30 K
RMSE
Root mean square error
0.9708
CV R² (mean)
5-fold cross-validation
Chart: Test R² by Model (higher = better)
| MLR | SVR | KNN | RF | ADA | DT
Test R² | 0.9641 | 0.9635 | 0.9577 | 0.9572 | 0.9519 | 0.9347
Chart: Test MAE in Kelvin (lower = better)
| MLR | SVR | RF | KNN | ADA | DT
MAE (K) | 3.43 | 3.44 | 3.7 | 3.77 | 3.97 | 4.45

## Slide 13
13 / 17
Applications
Where do we use predicted temperature?
⚡ Efficiency Loss Estimation
P(T) = P_STC × [1 + γ(T_max − 298)]
γ = −0.0045/K
At 350 K → ~23% power loss
🌡 Overheating Detection
Compare predicted vs threshold
(e.g., 370 K). Alert if breached.
Detect cell degradation early.
📡 Real-Time Onboard Prediction
Only 2 sensor inputs needed.
Lightweight — runs on ARM CPUs.
Continuous thermal state monitoring.
⚙ Design Optimisation
Evaluate 1,000s of configurations
in seconds. Replace repeated CFD
during design iteration.

## Slide 14
DASHBOARD
Deployed Web Dashboard
14 / 17
[ Dashboard Screenshot ]
APEX Solar · ML Analysis
Solar Panel Max Temperature
Prediction Dashboard
R² = 0.9641 | MAE = 3.425 K | RMSE = 4.303 K
Dashboard Features
3D Surface Plot
Interactive irradiation × T_amb vs T_max surface
Model Selector
Switch between all 6 models in real-time
Actual vs Predicted
Parity plot for test set accuracy
Residuals View
Error distribution analysis
All Models Overview
R², MAE, RMSE cards side-by-side
Performance Ranking
Ranked table with quality badges
🔗 manogna210524.github.io/Aerodynamic-Heating-on-Satellite-Solar-Panels/

## Slide 15
15 / 17
Conclusion
Key Takeaways
1
ANSYS simulation confirmed silicon cells as the primary heat source, with radiation to deep space as the only cooling path — validating the feature importance found by ML.
2
Multiple Linear Regression achieved the best performance (Test R² = 0.9641, MAE = 3.43 K, CV R² = 0.9708 ± 0.0024) — explaining 96.4% of panel temperature variance.
3
All 6 models achieved R² > 0.93, confirming that irradiation and ambient temperature are sufficient predictors of panel maximum temperature.
4
An interactive dashboard was deployed on GitHub Pages, enabling real-time thermal prediction and visual comparison of all 6 models.

## Slide 16
FUTURE SCOPE
Future Scope
16 / 17
🔬 CFD + ML Integration
Run parametric ANSYS sweep (irradiation 200–1,400 W/m², temp 260–320 K) → generate high-fidelity CFD dataset → train true CFD surrogate model.
🧠 Neural Network Surrogate
Multi-layer feedforward network (2 → 64 → 64 → 1) to better capture nonlinear thermal behaviour at high irradiation values (> 1,000 W/m²).
🛰 Onboard Spacecraft Implementation
Convert trained MLR to C/C++ for radiation-hardened ARM processors. Only 2 multiply-add ops — negligible compute overhead for continuous monitoring.
⚛ Physics-Informed ML (PIML)
Embed Stefan-Boltzmann radiation balance as a training constraint → improved extrapolation beyond training data range.

## Slide 17
Thank You
Questions & Discussion
1,757
Dataset samples
6
Models compared
0.9641
Best Test R²
3.43 K
Best MAE
🔗 manogna210524.github.io/Aerodynamic-Heating-on-Satellite-Solar-Panels/
APEX | B.Tech Project 2025–26 | Ramaraju · Sri Varsha · Manogna · Praneetha